## Slide 1: DIC Final Project
系所:電子所
組員:詹佳豐(312510075)
陸柏融(312510038)
施沛萱(312510023)
宋嘉祥(311510102)
宋彥霆(312510017)
1

## Slide 2: Content
Design of Pattern
Pattern Optimization
Digital CIM Macro Design
  pipeline (w/o pipeline vs w/ 1 cut, 2 cuts, 3 cuts)
  buffer dimension (1D,2D,3D)
  pattern w/o In_weight_x(x=1~32) vs w/ In_weight_x(x=1~32)
  clk period
  FSM (with FSM vs without FSM)
Discussion
  Area saturation effect
  The best design
Summary
2
Notes: 首先我會先介紹使用的pattern，然後設計各種不同的code，並逐一討論不同變因夏對於數據的影響，並將所有因素考慮後，找出最佳設計。

## Slide 3: Design of Pattern
3
Notes: 因final project 要求需要使IFM改變50次，因此在編寫Pattern時我們參考第五次作業的Pattern進行修正，上圖的i控制IFM的值可變化50次

## Slide 4: Design of Pattern
file_handle_1 = $fopen("test_weight.txt", "r");:
Open a text file named "test_weight.txt" and assign its file handle to the variable file_handle_1.
"r" indicates that the file is opened in read mode.
if (file_handle_1 != 0) begin:
Check if the file was successfully opened. If file_handle_1 is not equal to 0, indicating a successful opening, then enter the begin and end block.
4
Notes: 如圖所示，為了引入助教規定的input值，我們使用以上方式編入Pattern_ifm與Pattern_weight，同時我們也將答案的值編入Pattern_ofm裡，並宣告，當我們使用.v檔模擬的答案與Pattern_ofm相同時才會跑出成功圖，反之則會
失敗。
打開一個名為"test_weight.txt"的文本檔案，並將其文件控制代碼（file handle）賦值給變數file_handle_1。
"r"表示以讀取模式（read mode）打開文件。
檢查文件是否成功打開。如果file_handle_1不等於0，表示文件成功打開，則進入begin和end之間的區塊。

## Slide 5: Design of Pattern
cnt_1 = $fscanf(file_handle_1, "%d", Pattern_weight[i]);:
Use the $fscanf function to read an integer (%d) from the opened file.
The read data is stored in the Pattern_weight[i] array, where i is the current loop index.
cnt_1 is a counter, indicating the number of successfully read data.
$fclose(file_handle_1);:
Close the opened file, releasing associated resources.
5
Notes: 我們將助教的pattern灌入我們寫入的pattern，已取得IFM和Weight，經過Convolution.v運算後和助教的answer做比較。
使用$fscanf函數從打開的文件中讀取一個整數（%d）。
讀取的數據被賦值給Pattern_weight[i]，其中i是當前的迴圈索引。
cnt_1是一個計數器，用來表示成功讀取的數據個數。
關閉打開的文件，釋放資源。
總的來說，這段程式碼用於打開一個文本檔案，讀取其中的32個整數，並將它們存儲在Pattern_weight陣列中。如果文件成功打開，則會在迴圈結束後將文件關閉。 同理編寫pattern_ifm與pattern_ofm

## Slide 6: Pattern Optimization
we observe that the weight in pattern is always same, so we design to let weight receive value at convolution.v file
6
Notes: 因為weight的值並不會改變，因此我們決定不使用暫存器儲存weight值，而是直接將weight宣告為如右圖的形式。這樣的改變，可以預期最後得出的面積將會變小許多，進而提升area efficiency。

## Slide 7: IFM Waveform
7
Notes: 這是我們使用有weight buffer的pattern所模擬出來的結果，如圖所示，IFM中的數值與助教規定的數值相同

## Slide 8: Weight Waveform
8
Notes: 同理，weight也是助教規定的數值

## Slide 9: Out_OFM
9
Notes: Out_OFM waveform也符合助教所提供的answer sheet

## Slide 10: IFM & Out_OFM
10
Notes: 這是我們使用沒有weight buffer的pattern所模擬出來的結果，如圖所示，IFM中的數值也與助教規定的數值相同

## Slide 11: Digital CIM Macro Design
Without pipeline
I1
W1
I2
W2
I32
W32
X
X
X
.
.
.
.
+
+
I31
W31
X
.
.
.
.
.
.
.
.
.
.
.
.
.
Output
.
.
.
.
.
.
.
+
11
Notes: without pipeline透過直接將IFM和Weight相乘後再做相加的運算，直接得到Output。

## Slide 12: Digital CIM Macro Design
With pipeline (one cut on multiplier)
I1
W1
I2
W2
I32
W32
X
X
X
.
.
.
.
+
+
I31
W31
X
.
.
.
.
.
.
.
.
.
.
.
.
.
Output
Mul_Buffer[0]
Mul_Buffer[1]
Mul_Buffer[30]
Mul_Buffer[31]
+
...
.
.
.
...
.
.
.
12
Notes: 接著是With pipeline的架構，此圖為切一刀的情況， 和without pipeline相比下，我們多增加了32組Mul_Buff站存器。

## Slide 13: Digital CIM Macro Design
With pipeline (two cuts on multiplier and adder)
I1
W1
I2
W2
I32
W32
X
X
X
.
.
.
.
+
+
I31
W31
X
.
.
.
.
.
.
.
.
.
.
.
.
.
Output
Mul_Buffer[0]
Mul_Buffer[1]
Mul_Buffer[30]
Mul_Buffer[31]
+
Adder_Buffer[0]
Adder_Buffer[15]
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
..
.
.
.
.
.
..
.
.
.
13
Notes: 此圖為With pipeline(切兩刀)的架構圖: 如圖所示，和切一刀相比又多增加了16組Adder_Buffer。

## Slide 14: Digital CIM Macro Design
With pipeline (three cuts on multiplier, adder and adder1)
I1
W1
I2
W2
I32
W32
X
X
X
.
.
.
.
+
+
I31
W31
X
.
.
.
.
.
.
.
.
.
.
.
.
.
Output
Mul_Buffer[0]
Mul_Buffer[1]
Mul_Buffer[30]
Mul_Buffer[31]
+
Adder_Buffer[0]
Adder_Buffer[15]
.
.
.
.
.
.
..
.
.
.
.
.
..
.
.
.
Adder_Buffer[1]
Adder_Buffer[14]
+
Adder_Buffer1[0]
+
Adder_Buffer1[7]
..
.
..
.
.
.
14
Notes: 最後則是With pipeline切三刀的架構， 如圖所示，相較於切二刀來說，他多了八組Addbuffer1.

## Slide 15: Comparing the Impact of the Presence or Absence of Pipelining on Simulation Results
one cut on multiplier vs two cuts on multiplier and adder
2d buffer + without In_weight_x + no FSM |  |  |  |  |  |  | 
 | area(mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
one cut (clk period=645) | 6.84E-03 | 3.41E-08 | 3200 | 93.7948 | 13.7150 | 2.64E-03 | 3.55E+01
two cuts (clk period=565) | 8.19E-03 | 3.05E-08 | 3200 | 105.045 | 12.8209 | 3.27E-03 | 3.21E+01
15
Notes: 首先我們比較切一刀跟兩刀，分別在各自最小的clk period下進行模擬，顯而易見的，因為二刀使用了較多暫存器，所以一刀的面積必定小於二刀，但因為犧牲操作頻率，所以throughput低於切二刀，但因面積差具相較於throughput得差具來的多，導致面積對於area efficiency的影響加重。因此一刀的area efficiency大於二刀，而without pipeline 又少了更多暫存器，推測將會有最高的area efficiency。
而功率的部分我們認為應在同樣的頻率下做比較，如下一頁投影片展示。

## Slide 16: Comparing the Impact of the Presence or Absence of Pipelining on Simulation Results
without pipeline vs one cut on multiplier vs two cuts on multiplier and adder
2d buffer + without In_weight_x + no FSM + clk period =815 |  |  |  |  |  |  | 
 | area(mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
without | 3.20E-03 | 4.23E-08 | 3200 | 75.705599 | 23.634604 | 1.25E-03 | 6.08E+01
1 cuts | 5.77E-03 | 4.31E-08 | 3200 | 74.271788 | 12.865935 | 1.74E-03 | 4.28E+01
2 cuts | 7.15E-03 | 4.39E-08 | 3200 | 72.891278 | 10.201528 | 1.57E-03 | 4.65E+01
16
Notes: 在相同的clk period下，正如同預期，without pipeline的架構有最好的area efficiency，值得一提的是，在功率的部分也是without pipeline最低，推測是因為少跑了暫存器的緣故，

## Slide 17: Digital CIM Macro Design
17
Notes: 如圖，這是PATTERN在有weight buffer下去做切pipeline與無pipeline的比較，首先可以從面積知道說，weight buffer占了相當大的面積運算，跟後面沒有weight buffer時的面積基本上大了快兩倍，所以area efficiency 是無法贏過no PATTERN weight buffer，雖然從功耗層面來探討，沒有減少到多少，但足以判斷PATTERN weight buffer對於整體操作的影響，接下來比較有無切的情況，可以看到說，切pipeline的時候，可以將clk period往下調的幅度變大，亦即切pipeline可以操作在更短的operation time，因此對於througput有更傑出的表現。然而切pipeline會讓面積增加，功號上升，因此energy efficiency普遍低於without pipeline，這邊我們有觀察到當操作的clk period上升到某一個值時，area就不會再上升，就without pipeline數據為例 ，有特別把當下的clk period紅色註記起來，2D buffer是827ps，3D buffer則是839ps，詳細的介紹會在後面投影片。

## Slide 18: Digital CIM Macro Design
18
Notes: 此為優化後的pattern在without pipeline的throughput,area，energy efficiency的表現，我們觀察到without pipeline在經過某個特定的clk period後，area就不再變化，這樣會倒置隨著operation time的變長，最終讓throughtput的變差。

## Slide 19: Digital CIM Macro Design
19
Notes: 跟前述一致，如數據，切pipeline會讓面積增加，功號上升，因此energy efficiency普遍低於without pipeline。

## Slide 20: Digital CIM Macro Design
20
Notes: 此圖都使用2D buffer去進行比較，整體來說，在without pipeline下會擁有較高的area efficiency，如灰線和黃線所示，其中no代表著no pattern weight buffer，使area可以下降，而切pipeline會加入額外的暫存器，使area efficiency 下降。

## Slide 21: Digital CIM Macro Design
Buffer dimension:1D、2D、3D Buffer demostration
1D:
2D:
3D:
21
Notes: 接下來，我們嘗試將buffer 以1D、2D、3D的方式存取，去探討面積和power的變化

## Slide 22: Digital CIM Macro Design
Buffer dimension: 1D vs 2D vs 3D
 | area(mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
1D👑 | 6.65E-03 | 3.41E-08 | 3200 | 93.7948 | 14.1092 | 2.61E-03 | 3.60E+01
2D | 6.84E-03 | 3.41E-08 | 3200 | 93.7948 | 13.7150 | 2.64E-03 | 3.55E+01
3D | 6.90E-03 | 3.41E-08 | 3200 | 93.7948 | 13.5871 | 2.72E-03 | 3.45E+01
22
Notes: 根據上表，可以發現，在相同控制變因，固定pipeline數為一刀、clk period(645ps)、without pattern weight buffer、no fsm下，隨著維度的下降，模擬結果的面積與功耗都有微服下降，使得area efficiency與energy efficiency都有些微的提升。

## Slide 23: Digital CIM Macro Design
Buffer dimension comparison result
2D VS 3D: At same period, they have same operation time, but 3D area and power is higher than 2D
2D buffer is better than 3D
1D VS 2D: At same period, 1D area and power is smaller than 2D
1D buffer is better than 2D
1D buffer is the best of all !!
23
Notes: 我們認為以32組 IFM 和 Weight下， 在相同period下，剛好在1D buffer 的空間利用率會達到最高(優於2D、3D buffer)，推測合成出的電路並排和串聯的排列會是最小，以結果來看是1D最優

## Slide 24: Digital CIM Macro Design
PATTERN without In_weight_x(x=1~32) vs with In_weight_x(x=1~32)
result:
Because of reduction of the In_weight_x, the pattern without In_weight_x has smaller area
Area efficiency and the energy efficiency can be better
24
Notes: 因為省掉了pattern 內的weight buffer面積，所以Area efficiency和energy efficiency會比較高

## Slide 25: Digital CIM Macro Design
PATTERN without In_weight_x(x=1~32) vs with In_weight_x(x=1~32)
 | area(mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
With | 8.09E-03 | 3.26E-08 | 3200 | 98.120381 | 12.132923 | 2.98E-03 | 3.29E+01
Without | 1.11E-02 | 3.26E-08 | 3200 | 98.120381 | 8.8016251 | 3.56E-03 | 2.76E+01
25
Notes: 根據上表，可以發現如同預期，在相同控制變因((pipeline數(一刀)、clk period(605)、2d buffer、no fsm))下，pattern少了weight buffer的模擬結果，面積與功耗都有一定程度的下降，使得area efficiency與energy efficiency都有顯著的提升。值得一提的是，因為是操作在相同的clk period，因此throughput相同。

## Slide 26: Digital CIM Macro Design
clk period
With pipeline, we can decrease the clock period
Advantage: increase throughput and area efficiency
Disadvantage: increase area and power，decrease energy efficiency
26
Notes: 接下來討論使用with pipeline 的優缺點是可以降低clk period，operation time降低，增加throuput，area efficiency，
缺點是powe和面積的增加，進而降低energy efficiency，如下一張投影片的展示

## Slide 27: Digital CIM Macro Design
W/ pipeline (切兩刀)+2Dbuffer +NoFSM | area (mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
clk period=605 | 8.09E-03 | 3.26E-08 | 3200 | 98.12038144 | 12.13292355 | 2.98E-03 | 3.29E+01
clk period=600 | 8.04E-03 | 3.23E-08 | 3200 | 99.10188913 | 12.32432503 | 3.02E-03 | 3.28E+01
clk period=585 | 8.13E-03 | 3.15E-08 | 3200 | 101.4648995 | 12.47988599 | 3.13E-03 | 3.24E+01
clk period=565 | 8.19E-03 | 3.05E-08 | 3200 | 105.045465 | 12.82096052 | 3.27E-03 | 3.21E+01
27
Notes: 上表討論改變clk period時對於模擬結果的影響， 可以發現表現各有千秋，隨著clk period的降低，operation time也隨之下降，隨然面積也會因此提升，但根據我們area efficiency
量測的結果 ，可以發現operation time的影響大於area的影響，而power的部分則是隨著clk period的降低而提升，因此較低的clk period有較低的energy efficiency

## Slide 28: Digital CIM Macro Design
Comparison between “with FSM” and “without FSM”
With FSM:
advantage: easy to control the behavior of each circuit block
disadvantage: larger area
Without FSM:
advantage: decrease area about 3000um^2，increase area efficiency，decrease power，
increase energy efficiency
(ex: The area of w/ pipeline+2D buffer decreases from 11000 um^2 to 8000um^2)
disadvantage: hard to control the behavior of each circuit block
28
Notes: 接下來討論有無FSM的影響，使用FSM控制電路的不同狀態，其優點是可以增加程式碼的可讀性，比較容易debug；缺點是會增加電路的面積
沒有使用FSM可大幅度減少電路的面積，降低power，增加area efficiency，energy efficiency；比較南debug

## Slide 29: Digital CIM Macro Design
W/ pipeline (2cuts) +2Dbuffer (clk period =565) | area (mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
Without FSM | 8.19E-03 | 3.05E-08 | 3200 | 105.045465 | 12.82096052 | 3.27E-03 | 3.21E+01
With FSM | 1.11E-02 | 3.05E-08 | 3200 | 105.045465 | 9.596726341 | 3.879E-3 | 2.71E+01
Comparison between “with FSM” and “without FSM”
29
Notes: 去掉FSM可減少大約3000um^2的面積，可提高area efficiency，energy efficiency。降低power。

## Slide 30: Digital CIM Macro Design
W/ pipeline (1cut)+ 2Dbuffer+No FSM (clk period =739) | area (mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
RVT | 8.68E-03 | 3.91E-08 | 3200 | 81.89169823 | 9.43E+0 | 2.36E-03 | 34.74735222
LVT | 1.00E-02 | 3.9816E-08 | 3200 | 80.36970062 | 7.993E+0 | 2.601E-03 | 30.89953888
Comparison between different libraries of “RVT” and “LVT”
30
Notes: 在相同clk period之下，使用RVT會比LVT更好，使用RVT的面積較小，throughput、area efficiency、energy efficiency較大，power較小。
但使用LVT的優點可操作到最低的clk period。

## Slide 31: Area saturation effect
Without pipeline + 1d buffer + without In_weight_x + no FSM |  |  |  |  |  |  | 
 | area (mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
Clk period(795) | 3.034E-3 | 4.12E-8 | 3200 | 77.61 | 25.578 | 1.26E-3 | 6.16E+1
Clk period(815) | 3.028E-3 | 4.23E-8 | 3200 | 75.71 | 25.000 | 1.23E-3 | 6.18E+1
Clk period(860) | 3.028E-3 | 4.45E-8 | 3200 | 71.84 | 23.723 | 1.16E-3 | 6.19E+1
Clk period(905) | 3.028E-3 | 4.69E-8 | 3200 | 68.19 | 22.519 | 1.10E-3 | 6.19E+1
31
Notes: 另外我們發現了一個有趣的現象，理論上，當clk period 上升時，area應該會隨之下降，但我們發現了過了某一頻率(我們稱為飽和點)後面積將不再改變如表所示，我們稱之為面積飽和效應，這樣的特性對於area efficiency是非常不理想的

## Slide 32: Digital CIM Macro Design
The best design:
Without pipeline + 1D buffer + no FSM + without In_weight_x + RVT cell library
(clk period=795)
has area efficiency and power consumption, which is the best design we discover
 | area (mm^2) | operation time(s) | operation | throughput (GOPS) | area efficiency (TOPS/mm^2) | power(W) | energy efficiency (TOPS/W)
W/O pipeline +1Dbuffer +No FSM (clk period =795) | 3.034E-3 | 4.12E-8 | 3200 | 77.61 | 25.578 | 1.2259E-3 | 61.6
32
Notes: 綜合上述，我們發現最好的設計是without pipeline+1D buffer+ no FSM + without in_weight_x + RVT cell library (clk period=795)

## Slide 33
33
Notes: 我們發現在量測POWER的時候，若沒有加入兩個.sldb檔，會出現兩個error，若加入此兩個檔案解掉error後會導致power極大福的上升，但為求數據嚴謹起見，本篇報告量測數據皆有引入此二檔案。

## Slide 34: Digital CIM Macro Design
Summary
We have tried numerous methods, including w/ & w/o FSM, w/o pipeline & w/ pipeline(1 cut、2 cuts、3 cuts), new pattern which w/o In_weight_X and old pattern, and different dimensions of buffer.
Eventually, we found that w/o pipeline + 1D buffer + new pattern(clk period=795) is the best design!!!!!
34
Notes: 我們沒有使用clock gating的原因是因為觀察助教提供的50組input和weight，其中0的數字不多，若使用clock gating稍微可降低power，但會使面積增加，因此area efficiency不會比較好。
/////我們也有發現換.db file的library，將rvt換成lvt，合出來的area efficiency和energy efficiency會比較優異，不過助教沒有提到能不能換library，所以就沒有就這部分去講解了。

## Slide 35: 謝謝老師和助教這學期的關照
35